## Slide 1
Intelligent AOM
Introduction
In the experimental setup the spectrum of an incoming laser beam is changed in an acousto-optical modulator (AOM) by interfering with an applied radio frequency (rf) signal coming from an arbitrary wave generator (AWG).
We want to predict the frequency spectrum given to the AWG by modeling the resulting frequency spectra given a desired, complex output spectrum which should be then produced by the AOM.
Project Donor: Dr. Prof. Eschner & Team (Experimental Physics – Quantum Photonics)
Leo Forster & Jonas Henker
Motivation [Image 1, Image 2]
For experiments in the field of quantum photonics concrete frequency spectra are often needed. Due to nonlinear and complex input-output relationships, the required AWG configurations can not be computed easily but by applying machine learning methods we can predict them to a certain accuracy. Doing so, we achieve the ability to control output frequency spectra freely, provided by the configurations given by our model.
Objectives
Find a suitable model able to predict the required AWG input spectra, given the desired AOM output spectra and observe the impact of different hyperparameters, changes in the simulation & non-linearity on the model performance.
Data Processing [Image 3]
Each AWG input spectrum has 11 real valued & 11 complex valued frequencies ranging from 95 to 105 mHz.
Similar, each AOM output spectrum has 101 real valued & 101 complex valued frequencies ranging from 50 to 150 mHz.
The training data is generated without noise and missing values.
For this we sample the potential AWG input spectra by randomly selecting points on the surface of a 22-dimensional sphere, ensuring that the norm is constant.
The AOM output is obtained by simulating the AOM using a provided mathematical model which is similar in complexity.
Using both the simulated AOM output spectra as input and the sampled AWG input spectra as desired output, we train the model.
Simplified Experimental Setup
Visualisation of Data Processing
DSAI Project Seminar
Image 1: Experimental Setup
Image 2
Image 3
Model Architecture
Results